## Slide 1: Tutorial Outline
Time | Topic
8:45 am – 9:00 am | Hands-on: Virtual Machine Setup
9:00 am – 9:20 am | Presentation: Accelerator Research Overview
9:20 am – 9:35 am | Presentation: Aladdin: Accelerator Pre-RTL Modeling
9:35 am – 10:15 am | Hands-on: Accelerator Design Space Exploration using Aladdin
10:15 am – 10:30 am | Break
10:30 am – 11:00 am | Presentation: gem5-Aladdin: Accelerator System Integration
11:00 am – 12:00 pm | Hands-on: SoC Design Space Exploration using gem5-Aladdin
Notes: Amortize optimization phase

## Slide 2
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator

## Slide 3
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Flexibility
Programmability
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator

## Slide 4
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Design Cost
Flexibility
Programmability
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator
“Design Assistant”
Understand Algorithmic-HW
Design Space before RTL

## Slide 5: Future Accelerator-Centric Architecture
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores

## Slide 6: Future Accelerator-Centric Architecture
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores
Aladdin can rapidly evaluate large design space of accelerator-centric architectures.

## Slide 7: Aladdin Overview
C Code
Power/Area
Performance
Activity
Acc Design Parameters
Optimization Phase
Realization Phase
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Dynamic Data
Dependence Graph
(DDDG)

## Slide 8: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 9: From C to Design Space
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];

## Slide 10: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 11: From C to Design Space IR Dynamic Trace
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
0. r0=0 //i = 0
r4=load (r0 + r1) //load a[i]
r5=load (r0 + r2) //load b[i]
r6=r4 + r5
store(r0 + r3, r6) //store c[i]
r0=r0 + 1 //++i
r4=load(r0 + r1) //load a[i]
r5=load(r0 + r2) //load b[i]
r6=r4 + r5
store(r0 + r3, r6) //store c[i]
r0 = r0 + 1 //++i
…

## Slide 12: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 13: From C to Design Space Initial DDDG
0. i=0
1. ld a
2. ld b
3. +
4. st c
5. i++
6. ld a
7. ld b
8. +
9. st c
10. i++
11. ld a
12. ld b
13. +
14. st c
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
IR Trace:
0. r0=0 //i = 0
1. r4=load (r0 + r1) //load a[i]
2. r5=load (r0 + r2) //load b[i]
3. r6=r4 + r5
4. store(r0 + r3, r6) //store c[i]
5. r0=r0 + 1 //++i
6. r4=load(r0 + r1) //load a[i]
7. r5=load(r0 + r2) //load b[i]
8. r6=r4 + r5
9. store(r0 + r3, r6) //store c[i]
10.r0 = r0 + 1 //++i
…

## Slide 14: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 15: From C to Design Space Idealistic DDDG
0. i=0
5. i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
IR Trace:
0. r0=0 //i = 0
1. r4=load (r0 + r1) //load a[i]
2. r5=load (r0 + r2) //load b[i]
3. r6=r4 + r5
4. store(r0 + r3, r6) //store c[i]
5. r0=r0 + 1 //++i
6. r4=load(r0 + r1) //load a[i]
7. r5=load(r0 + r2) //load b[i]
8. r6=r4 + r5
9. store(r0 + r3, r6) //store c[i]
10.r0 = r0 + 1 //++i
…
0. i=0
5. i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c

## Slide 16: From C to Design Space Idealistic DDDG
Include application-specific customization strategies.
Node-Level:
  Bit-width Analysis
  Strength Reduction
  Tree-height Reduction
Loop-Level:
  Remove dependences between loop index variables
Memory Optimization:
  Memory-to-Register Conversion
  Store-Load Forwarding
  Store Buffer
Extensible
  e.g. Model CAM accelerator by matching nodes in DDDG

## Slide 17: Aladdin Overview
Power/Area
Models
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 18: From C to Design Space One Design
MEM
MEM
MEM
MEM
MEM
MEM
+
+
+
Resource Activity
Idealistic DDDG
Acc Design Parameters:
Memory BW <= 2
1 Adder
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c
Cycle
0. i=0
5.i++
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c

## Slide 19: From C to Design Space Another Design
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
+
+
+
+
+
+
+
Resource Activity
Cycle
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c
6. ld a
Acc Design Parameters:
Memory BW <= 4
2 Adders
Idealistic DDDG
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c

## Slide 20: From C to Design Space Realization Phase: DDDG->Power-Perf
Constrain the DDDG with program and user-defined resource constraints
Program Constraints
  Control Dependence
  Memory Ambiguation
Resource Constraints
  Loop-level Parallelism
  Loop Pipelining
  Memory Ports

## Slide 21: From C to Design Space Power-Performance per Design
Cycle
Power
Acc Design Parameters:
Memory BW <= 4
2 Adders
Acc Design Parameters:
Memory BW <= 2
1 Adder

## Slide 22: From C to Design Space Design Space of an Algorithm
Cycle
Power

## Slide 23: Power Model
Functional Units Power Model
  Microbenchmarks characterize various FUs.
  Design Compiler with 40nm Standard Cell
SRAM Power Model
  Commercial register file and SRAM memory compilers with the same 40nm standard cell library

## Slide 24: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 25: Aladdin Validation
C Code
Power/Area Performance
Aladdin
ModelSim
Design
Compiler
Verilog
Activity

## Slide 26: Aladdin Validation
C Code
Power/Area Performance
Aladdin
RTL Designer
HLS C Tuning
Vivado
HLS
ModelSim
Design
Compiler
Verilog
Activity

## Slide 27: Aladdin Validation

## Slide 28: Aladdin Validation

## Slide 29: Aladdin enables rapid design space exploration for accelerators.
C Code
Power/Area Performance
Aladdin
RTL Designer
HLS C Tuning
Vivado
HLS
ModelSim
Design
Compiler
Verilog
Activity
7 mins
52 hours

## Slide 30: Limitations
Algorithm Choices
  Aladdin generates a design space per algorithm
  Can use Aladdin to quickly compare the design spaces of algorithms
Input Dependent
  Inputs that exercise all paths of the code
Input C Code
  Aladdin can create DDDG for any C code.
  C constructs that require resources outside the accelerator, such as system calls and dynamic memory allocation, are not modeled.

## Slide 31: Aladdin enables pre-RTL simulation of accelerators with the rest of the SoC.
GPU
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Big
Cores
Small Cores
GPGPU-Sim
gem5
...
gem5
…
Cacti/Orion2
DRAMSim2

## Slide 32: Aladdin: A pre-RTL, Power-Performance Accelerator Simulator
Architectures with 1000s of accelerators will be radically different; New design tools are needed.
Aladdin enables rapid design space exploration of future accelerator-centric platforms.
Download Aladdin at
http://vlsiarch.eecs.harvard.edu/aladdin

## Slide 33: Tutorial Outline
Time | Topic
8:45 am – 9:00 am | Hands-on: Virtual Machine Setup
9:00 am – 9:20 am | Presentation: Accelerator Research Overview
9:20 am – 9:35 am | Presentation: Aladdin: Accelerator Pre-RTL Modeling
9:35 am – 10:15 am | Hands-on: Accelerator Design Space Exploration using Aladdin
10:15 am – 10:30 am | Break
10:30 am – 11:00 am | Presentation: gem5-Aladdin: Accelerator System Integration
11:00 am – 12:00 pm | Hands-on: SoC Design Space Exploration using gem5-Aladdin

## Slide 34: Aladdin Hands-on Exercise
Goal:
  Running a power-performance design space exploration for stencil2d in MachSuite.
Tasks:
  Build LLVM-Tracer, Aladdin, and verify with aladdin unit-tests.
  Walk through the design space exploration steps using triad as an example:
    Generate LLVM IR trace
    Prepare a hardware configuration file
    Run Aladdin
    Explore the parameter space
      Unrolling
      Memory Bandwidth
      Clock frequency
  Repeat the above steps for MachSuite/stencil2d

## Slide 35: Task 1: Build LLVM-Tracer and Aladdin
Make sure LLVM-Tracer and Aladdin are built successfully in your virtual machine.

## Slide 36: Task 2 Design Space Exploration for triad
void triad (int *a, int *b, int *c, int s) {
int i;
triad_loop: for (i = 0; i < NUM; i++) {
c[i] = a[i] + s * b[i];
}
}

## Slide 37: Task 2 Design Space Exploration for triad
void triad (int *a, int *b, int *c, int s) {
int i;
triad_loop: for (i = 0; i < NUM; i++) {
c[i] = a[i] + s * b[i];
}
}
Arrays

## Slide 38: Task 2 Design Space Exploration for triad
void triad (int *a, int *b, int *c, int s) {
int i;
triad_loop: for (i = 0; i < NUM; i++) {
c[i] = a[i] + s * b[i];
}
}
Arrays
Loop

## Slide 39: Array Parameters
Read port
Write port
Partition/Bank
partition,cyclic,a,8192,4,1
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 1 (1 partition)

## Slide 40: Array Parameters
Read port
Write port
Partition/Bank
partition,cyclic,a,8192,4,1
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 1 (1 partition)
partition,cyclic,a,8192,4,2
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 2 (2 partitions)

## Slide 41: Array Parameters
Read port
Write port
Partition/Bank
partition,cyclic,a,8192,4,2
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 2 (2 partitions)
a[0]
a[1]
a[2]
a[3]
partition,block,a,8192,4,2
// partition type: block
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 2 (2 partitions)
a[0]
a[2]
a[1]
a[3]

## Slide 42: Loop Parameters
a
b
s
c
X
+
unrolling,triad,triad_loop,1
// unrolling a loop
// function name : triad
// loop label : triad_loop
// unrolling factor : 1

## Slide 43: Loop Parameters
a
b
s
c
X
+
a
b
s
c
X
+
unrolling,triad,triad_loop,2
// unrolling a loop
// function name : triad
// loop label : triad_loop
// unrolling factor : 2

## Slide 44: Task 2.1 Generator Triad Trace
vagrant@genie:~$ cd gem5-aladdin/src/aladdin/SHOC/triad/
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$ vi triad.c
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$ make run-trace
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$
vi dynamic_trace.gz

## Slide 45: Task 2.2 Setup a design config
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$ mkdir example
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$ vi triad.cfg

## Slide 46: Task 2.2 Setup a design config
cycle_time,6
pipelining,1
partition,cyclic,a,8192,4,1
partition,cyclic,b,8192,4,1
partition,cyclic,c,8192,4,1
unrolling,triad,triad_loop,1

## Slide 47: Task 2.2 Setup a design config
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$
cp ../run.sh .
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$ make outputs
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$ bash run.sh

## Slide 48: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 |  | 

## Slide 49: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 4.47
4 | 1 | 6 | 2052 | 4.43
4 | 4 | 6 | 516 | 10.29
4 | 4 | 1 | 517 | 68.91

## Slide 50: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 4.47
4 | 1 | 6 | 2052 | 4.43
4 | 4 | 6 | 516 | 10.29
4 | 4 | 1 | 517 | 68.91

## Slide 51: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 4.47
4 | 1 | 6 | 2052 | 4.43
4 | 4 | 6 | 516 | 10.29
4 | 4 | 1 | 517 | 68.913

## Slide 52: Tutorial Outline
Time | Topic
8:45 am – 9:00 am | Hands-on: Virtual Machine Setup
9:00 am – 9:20 am | Presentation: Accelerator Research Overview
9:20 am – 9:35 am | Presentation: Aladdin: Accelerator Pre-RTL Modeling
9:35 am – 10:15 am | Hands-on: Accelerator Design Space Exploration using Aladdin
10:15 am – 10:30 am | Break
10:30 am – 11:00 am | Presentation: gem5-Aladdin: Accelerator System Integration
11:00 am – 12:00 pm | Hands-on: SoC Design Space Exploration using gem5-Aladdin
Notes: Amortize optimization phase