## Slide 1: Tutorial Outline
Time | Topic
9:00 am – 9:30 am | Introduction
9:30 am – 10:10 am | Standalone Accelerator Simulation: Aladdin
10:10 am – 10:30 am | Standalone Accelerator Generation: High-Level Synthesis
10:30 am – 11:00 am | HLS-Based Accelerator-Rich Architecture Simulation: PARADE
11:00 am – 11:30 am | Break
11:30 am – 12:00 pm | Pre-RTL SoC Simulation: gem5-Aladdin
12:00 pm – 12:30 pm | FPGA Prototyping: ARACompiler
12:30 pm – 2:00 pm | Lunch
2:00 pm – 3:00 pm | Panel on Accelerator Research
3:00 pm – 3:30 pm | Accelerator Benchmarks and Workload Characterization
3:30 pm – 4:00 pm | Break
4:00 pm – 5:00 pm | Hands-on Exercise
Notes: Amortize optimization phase

## Slide 2
A Pre-RTL, Power-Performance Accelerator Simulator Enabling Large Design Space Exploration of Customized Architectures
Yakun Sophia Shao, Brandon Reagen,
Gu-Yeon Wei, David Brooks Harvard University

## Slide 3: Today’s SoC
GPU/DSP
CPU
Buses
Mem
Inter-
face
Acc
CPU
Acc
Acc
Acc
Acc
Acc
Acc
Acc
Acc

## Slide 4: Future Accelerator-Centric Architectures
Flexibility
Design Cost
Programmability
How to decompose an application to accelerators?
How to rapidly design lots of accelerators?
How to design and manage the shared resources?
GPU/DSP
Big
Cores
Shared Resources
Memory
Interface
CGRA/
FPGA
Small Cores
Fine-
Grained
ASIC

## Slide 5
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator

## Slide 6
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Flexibility
Programmability
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator

## Slide 7
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Design Cost
Flexibility
Programmability
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator
“Design Assistant”
Understand Algorithmic-HW
Design Space before RTL

## Slide 8: Future Accelerator-Centric Architecture
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores

## Slide 9: Future Accelerator-Centric Architecture
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores
Aladdin can rapidly evaluate large design space of accelerator-centric architectures.

## Slide 10: Aladdin Overview
C Code
Power/Area
Performance
Activity
Acc Design Parameters
Optimization Phase
Realization Phase
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Dynamic Data
Dependence Graph
(DDDG)

## Slide 11: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 12: From C to Design Space
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];

## Slide 13: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 14: From C to Design Space IR Dynamic Trace
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
0. r0=0 //i = 0
r4=load (r0 + r1) //load a[i]
r5=load (r0 + r2) //load b[i]
r6=r4 + r5
store(r0 + r3, r6) //store c[i]
r0=r0 + 1 //++i
r4=load(r0 + r1) //load a[i]
r5=load(r0 + r2) //load b[i]
r6=r4 + r5
store(r0 + r3, r6) //store c[i]
r0 = r0 + 1 //++i
…

## Slide 15: Optimistic IR
LLVM IR
High-level IR:
  Machine- and ISA-independent
Features:
  Unlimited Registers
  Simple Opcodes: add, mul, sin, sqrt
  Only load/store access memory
Shao, et al., ISA-Independent Workload Characterization and Implications for Specialized Architecture,
ISPASS, 2013

## Slide 16: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 17: From C to Design Space Initial DDDG
0. i=0
1. ld a
2. ld b
3. +
4. st c
5. i++
6. ld a
7. ld b
8. +
9. st c
10. i++
11. ld a
12. ld b
13. +
14. st c
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
IR Trace:
0. r0=0 //i = 0
1. r4=load (r0 + r1) //load a[i]
2. r5=load (r0 + r2) //load b[i]
3. r6=r4 + r5
4. store(r0 + r3, r6) //store c[i]
5. r0=r0 + 1 //++i
6. r4=load(r0 + r1) //load a[i]
7. r5=load(r0 + r2) //load b[i]
8. r6=r4 + r5
9. store(r0 + r3, r6) //store c[i]
10.r0 = r0 + 1 //++i
…

## Slide 18: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 19: From C to Design Space Idealistic DDDG
0. i=0
5. i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
IR Trace:
0. r0=0 //i = 0
1. r4=load (r0 + r1) //load a[i]
2. r5=load (r0 + r2) //load b[i]
3. r6=r4 + r5
4. store(r0 + r3, r6) //store c[i]
5. r0=r0 + 1 //++i
6. r4=load(r0 + r1) //load a[i]
7. r5=load(r0 + r2) //load b[i]
8. r6=r4 + r5
9. store(r0 + r3, r6) //store c[i]
10.r0 = r0 + 1 //++i
…
0. i=0
5. i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c

## Slide 20: From C to Design Space Idealistic DDDG
Include application-specific customization strategies.
Node-Level:
  Bit-width Analysis
  Strength Reduction
  Tree-height Reduction
Loop-Level:
  Remove dependences between loop index variables
Memory Optimization:
  Memory-to-Register Conversion
  Store-Load Forwarding
  Store Buffer
Extensible
  e.g. Model CAM accelerator by matching nodes in DDDG

## Slide 21: Aladdin Overview
Power/Area
Models
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 22: From C to Design Space One Design
MEM
MEM
MEM
MEM
MEM
MEM
+
+
+
Resource Activity
Idealistic DDDG
Acc Design Parameters:
Memory BW <= 2
1 Adder
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c
Cycle
0. i=0
5.i++
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c

## Slide 23: From C to Design Space Another Design
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
+
+
+
+
+
+
+
Resource Activity
Cycle
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c
6. ld a
Acc Design Parameters:
Memory BW <= 4
2 Adders
Idealistic DDDG
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c

## Slide 24: From C to Design Space Realization Phase: DDDG->Power-Perf
Constrain the DDDG with program and user-defined resource constraints
Program Constraints
  Control Dependence
  Memory Ambiguation
Resource Constraints
  Loop-level Parallelism
  Loop Pipelining
  Memory Ports
  # of FUs (e.g., adders, multipliers)

## Slide 25: Memory Ambiguation
Idealistic DDDG optimistically removes all false memory dependences
Input-dependent memory accesses cannot be calculated statically.

## Slide 26: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 1;
a[2] = 1;
…
3.ld b[1]
4.b[1]++
5.st b[1]

## Slide 27: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 2;
a[2] = 1;
…
3.ld b[1]
4.b[1]++
5.st b[1]
6.i++
7.ld a[1]
8.&
9.ld b[2]
10.b[2]++
11.st b[2]

## Slide 28: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 2;
a[2] = 2;
…
3.ld b[1]
4.b[1]++
5.st b[1]
6.i++
7.ld a[1]
8.&
9.ld b[2]
10.b[2]++
11.st b[2]
12.i++
13.ld a[2]
14.&
15.ld b[2]
16.b[2]++
17.st b[2]

## Slide 29: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 2;
a[2] = 2;
…
3.ld b[1]
4.b[1]++
5.st b[1]
6.i++
7.ld a[1]
8.&
9.ld b[2]
10.b[2]++
11.st b[2]
12.i++
13.ld a[2]
14.&
16.b[2]++
17.st b[2]
15.ld b[2]

## Slide 30: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 2;
a[2] = 2;
…
3.ld b[1]
4.b[1]++
5.st b[1]
6.i++
7.ld a[1]
8.&
9.ld b[2]
10.b[2]++
11.st b[2]
12.i++
13.ld a[2]
14.&
16.b[2]++
17.st b[2]
15.ld b[2]

## Slide 31: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 2;
a[2] = 2;
…
3.ld b[1]
4.b[1]++
6.i++
7.ld a[1]
8.&
10.b[2]++
11.st b[2]
12.i++
13.ld a[2]
14.&
16.b[2]++
17.st b[2]
15.ld b[2]
5.st b[1]
9.ld b[2]

## Slide 32: Memory Ambiguation
for(i=0; i<N; ++i)
{
bucket[ a[i] & 0x11 ]++;
}
0.i=0
1.ld a[0]
2.&
Input:
a[0] = 1;
a[1] = 2;
a[2] = 2;
…
3.ld b[1]
4.b[1]++
6.i++
7.ld a[1]
8.&
10.b[2]++
11.st b[2]
12.i++
13.ld a[2]
14.&
16.b[2]++
17.st b[2]
15.ld b[2]
5.st b[1]
9.ld b[2]

## Slide 33: From C to Design Space Power-Performance per Design
Cycle
Power
Acc Design Parameters:
Memory BW <= 4
2 Adders
Acc Design Parameters:
Memory BW <= 2
1 Adder

## Slide 34: From C to Design Space Design Space of an Algorithm
Cycle
Power

## Slide 35: Cycle-Level Activity

## Slide 36: Power Model
Functional Units Power Model
  Microbenchmarks characterize various FUs.
  Design Compiler with 40nm Standard Cell
SRAM Power Model
  Commercial register file and SRAM memory compilers with the same 40nm standard cell library

## Slide 37: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 38: Aladdin Validation
C Code
Power/Area Performance
Aladdin
ModelSim
Design
Compiler
Verilog
Activity

## Slide 39: Aladdin Validation
C Code
Power/Area Performance
Aladdin
RTL Designer
HLS C Tuning
Vivado
HLS
ModelSim
Design
Compiler
Verilog
Activity

## Slide 40: Validation Benchmarks
Type | Benchmark | Description
SHOC Benchmark Suite | MD | Pairwise calculation of the L-J Potential
 | STENCIL | Apply 3x3 filter to an image
 | FFT | 1D 512 FFT
 | GEMM | Blocked Matrix Multiply
 | TRIAD | Single Computation in DOALL loop
 | SORT | Radix Sort
 | SCAN | Parallel prefix sum
 | REDUCTION | Return sum of an array
Proposed Accelerator Constructs | NPU | An individual neuron in a network [MICRO’12]
 | Memcached | GET function in Memcached [ISCA’13]
 | HARP | Data partition accelerator [ISCA’13]
Optimized
HLS
Designs
Hand RTL
Designs

## Slide 41: Aladdin Validation

## Slide 42: Aladdin Validation

## Slide 43: Aladdin enables rapid design space exploration for accelerators.
C Code
Power/Area Performance
Aladdin
RTL Designer
HLS C Tuning
Vivado
HLS
ModelSim
Design
Compiler
Verilog
Activity
7 mins
52 hours

## Slide 44: Limitations
Algorithm Choices
  Aladdin generates a design space per algorithm
  Can use Aladdin to quickly compare the design spaces of algorithms
Input Dependent
  Inputs that exercise all paths of the code
Input C Code
  Aladdin can create DDDG for any C code.
  C constructs that require resources outside the accelerator, such as system calls and dynamic memory allocation, are not modeled.

## Slide 45: Aladdin enables pre-RTL simulation of accelerators with the rest of the SoC.
GPU
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Big
Cores
Small Cores
GPGPU-Sim
gem5
...
gem5
…
Cacti/Orion2
DRAMSim2

## Slide 46: Aladdin: A pre-RTL, Power-Performance Accelerator Simulator
Architectures with 1000s of accelerators will be radically different; New design tools are needed.
Aladdin enables rapid design space exploration of future accelerator-centric platforms.
Download Aladdin at
http://vlsiarch.eecs.harvard.edu/aladdin

## Slide 47: Tutorial References
Y.S. Shao and D. Brooks, “ISA-Independent Workload Characterization and its Implications for Specialized Architectures,” ISPASS’13.
B. Reagen, Y.S. Shao, G.-Y. Wei, D. Brooks, “Quantifying Acceleration: Power/Performance Trade-Offs of Application Kernels in Hardware,” ISLPED’13.
Y.S. Shao, B. Reagen, G.-Y. Wei, D. Brooks, “Aladdin: A Pre-RTL, Power-Performance Accelerator Simulator Enabling Large Design Space Exploration of Customized Architectures,” ISCA’14.
B. Reagen, B. Adolf, Y.S. Shao, G.-Y. Wei, D. Brooks, “MachSuite: Benchmarks for Accelerator Design and Customized Architectures,” IISWC’14.