## Slide 1: Tutorial Outline
Time | Topic | Speaker
8:30 am – 9:00 am | Accelerator Research Infrastructure Overview | Sophia Shao
9:00 am – 9:30 am | Aladdin: Accelerator Pre-RTL Modeling | Sophia Shao
9:30 am – 10:00 am | Rapid Hardware Specialization with HLS: Glass Half Full | Prof. Zhiru Zhang
10:00 am – 10:30 am | PARADE: HLS-Based Accelerator-Rich Architecture Simulation | Zhenman Fang
10:30 am – 11:00 am | Break | 
11:00 am – 11:30 am | gem5-Aladdin: Accelerator System Co-Design | Sam Xi
11:30 am – 12:00 pm | ARAPrototyper: FPGA Prototyping | Zhenman Fang
12:00pm – 13:30 pm | Lunch | 
13:30 pm – 14:00 pm | Virtual Machine Setup | Sophia Shao & Sam Xi
14:00 pm – 14:30 pm | Hands-on: Accelerator Design Space Exploration using Aladdin | Sophia Shao
14:30 pm – 15:00 pm | Hands-on: SoC Design Space Exploration using gem5-Aladdin | Sam Xi
Notes: Amortize optimization phase

## Slide 2: Aladdin Hands-on Exercise
Goal:
  Running a power-performance design space exploration for triad in MachSuite.
Tasks:
  Build LLVM-Tracer, Aladdin, and verify with aladdin unit-tests.
  Walk through the design space exploration steps using triad as an example:
    Generate LLVM IR trace
    Prepare a hardware configuration file
    Run Aladdin
    Explore the parameter space
      Unrolling
      Memory Bandwidth
      Clock frequency
  Repeat the above steps for MachSuite/stencil2d

## Slide 3: Task 1: Build LLVM-Tracer and Aladdin
Make sure LLVM-Tracer and Aladdin are built successfully in your virtual machine.

## Slide 4: Task 2 Design Space Exploration for triad
void triad (int *a, int *b, int *c, int s) {
int i;
triad_loop: for (i = 0; i < NUM; i++) {
c[i] = a[i] + s * b[i];
}
}

## Slide 5: Task 2 Design Space Exploration for triad
void triad (int *a, int *b, int *c, int s) {
int i;
triad_loop: for (i = 0; i < NUM; i++) {
c[i] = a[i] + s * b[i];
}
}
Arrays

## Slide 6: Task 2 Design Space Exploration for triad
void triad (int *a, int *b, int *c, int s) {
int i;
triad_loop: for (i = 0; i < NUM; i++) {
c[i] = a[i] + s * b[i];
}
}
Arrays
Loop

## Slide 7: Array Parameters
Read port
Write port
Partition/Bank
partition,cyclic,a,8192,4,1
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 1 (1 partition)

## Slide 8: Array Parameters
Read port
Write port
Partition/Bank
partition,cyclic,a,8192,4,1
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 1 (1 partition)
partition,cyclic,a,8192,4,2
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 2 (2 partitions)

## Slide 9: Array Parameters
Read port
Write port
Partition/Bank
partition,cyclic,a,8192,4,2
// partition type: cyclic
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 2 (2 partitions)
a[0]
a[1]
a[2]
a[3]
partition,block,a,8192,4,2
// partition type: block
// array name : a
// array size : 8192 Bytes
// element size : 4 Bytes (int)
// partition factor : 2 (2 partitions)
a[0]
a[2]
a[1]
a[3]

## Slide 10: Loop Parameters
a
b
s
c
X
+
unrolling,triad,triad_loop,1
// unrolling a loop
// function name : triad
// loop label : triad_loop
// unrolling factor : 1

## Slide 11: Loop Parameters
a
b
s
c
X
+
a
b
s
c
X
+
unrolling,triad,triad_loop,2
// unrolling a loop
// function name : triad
// loop label : triad_loop
// unrolling factor : 2

## Slide 12: Task 2.1 Generator Triad Trace
vagrant@genie:~$ cd gem5-aladdin/src/aladdin/SHOC/triad/
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$ vi triad.c
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$ make run-trace
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$
vi dynamic_trace.gz

## Slide 13: Task 2.2 Setup a design config
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad$ mkdir example
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$ vi triad.cfg

## Slide 14: Task 2.2 Setup a design config
cycle_time,6
pipelining,1
partition,cyclic,a,8192,4,1
partition,cyclic,b,8192,4,1
partition,cyclic,c,8192,4,1
unrolling,triad,triad_loop,1

## Slide 15: Task 2.2 Setup a design config
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$
cp ../run.sh .
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$ mkdir outputs
vagrant@genie:~/gem5-aladdin/src/aladdin/SHOC/triad/example$ bash run.sh

## Slide 16: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 

## Slide 17: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 
4 | 1 | 6 | 2052 | 
4 | 4 | 6 | 516 | 10.2888
4 | 4 | 1 | 517 | 68.91

## Slide 18: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 4.47
4 | 1 | 6 | 2052 | 4.43
4 | 4 | 6 | 516 | 10.29
4 | 4 | 1 | 517 | 68.91

## Slide 19: Task 2.3 Design Space Exploration
Unrolling | Partition | Clock Period (ns) | Cycles | Power (mW)
1 | 1 | 6 | 2052 | 4.47
4 | 1 | 6 | 2052 | 4.43
4 | 4 | 6 | 516 | 10.29
4 | 4 | 1 | 517 | 68.91